## Slide 1
Indoor Environment Mapping Tutorials
Adding Realsense R200 camera to ARDrone in Gazebo7

## Slide 2: Required ROS Packages
For simulation of ARDrone in Gazebo
  ardrone_simulator_gazebo7 [2] - [1]
For simulation of Realsense R200 in Gazebo
  realsense_gazebo_plugin [2] - [1]

## Slide 3: URDF File format
The Universal Robotic Description Format (URDF) is an XML file format used in ROS to describe all elements of a robot
URDF can only specify the kinematic and dynamic properties of a single robot in isolation. URDF can not specify the pose of the robot itself within a world
URDF is the main file format used in ROS and visualisation RViz

## Slide 4: SDF File format
SDF is an XML format that describes objects and environments for robot simulators, visualisation, and control
Originally developed as part of the Gazebo robot simulator, SDF is a substitute for the URDF format and solves the shortcomings of the URDF format
SDF format is capable of describing all aspects of robots, static and dynamic objects, lighting, terrain, and even physics.
SDF is the main file format supported by Gazebo

## Slide 5: Challenge
The realsense_gazebo_plugin package provides the Realsense R200 camera in SDF format
The ardrone_simulator_gazebo7 package provides the ARDrone in URDF format
The two formats are incompatible with each other and hence one file format needs to be converted to the other

## Slide 6: Solution
Launch ardrone_testworld.launch (cvg_sim_gazebo package) to spawn the URDF of the ARDrone in Gazebo
Add the Realsense R200 camera into the same world from the insert tab in the left pane of Gazebo
Save this world from the file menu in Gazebo in .world format

## Slide 7: Solution
In the world file (which is of SDF format) the Realsense camera as well as the ARDrone will be defined as models.
Make Realsense camera model nested inside the ARDrone model and edit the pose tag to place it at the appropriate position. Also create a fixed joint between the two models. Refer to [3]

## Slide 8: Appendix
Github Link for packages - https://github.com/eYSIP-2017/eYSIP-2017_Indoor-Environments-Mapping-using-UAV
Link to install Gazebo7 - https://github.com/eYSIP-2017/eYSIP-2017_Indoor-Environments-Mapping-using-UAV/blob/master/bash_scripts/install_gazebo7.sh
Tutorial for nested model and joint - http://gazebosim.org/tutorials?tut=nested_model&cat=build_robot#Joints
Link to final world file - https://github.com/eYSIP-2017/eYSIP-2017_Indoor-Environments-Mapping-using-UAV/blob/master/realsense_gazebo_plugin/worlds/ardrone_realsense.world

## Slide 9: References
http://gazebosim.org/tutorials/?tut=ros_urdf
http://sdformat.org

## Slide 10
THANK YOU!