## Slide 1
Indoor Environment Mapping Tutorials
Using RTAB-Map for mapping with Kinect

## Slide 2: Required ROS Packages
For interfacing Kinect with ROS
  libfreenect - sudo apt-get install libfreenect-dev
  freenect_launch - sudo apt-get install ros-indigo-freenect-launch
For RTAB-Map with ROS
  rtabmap_ros - sudo apt-get install ros-indigo-rtabmap-ros

## Slide 3: RTAB-Map
Simultaneous Localisation And Mapping (SLAM) is the computational problem of constructing or updating a map of an unknown environment while simultaneously keeping track of an agent's location within it
RTAB-Map (Real-Time Appearance-Based Mapping) is a RGB-D Graph-Based SLAM approach based on an incremental appearance-based loop closure detector
RTAB-Map can be used alone with a hand-held Kinect or stereo camera for 6DoF RGB-D mapping

## Slide 4: Procedure
Connect Kinect camera to PC/Laptop
Run “roslaunch freenect_launch freenect.launch depth_registration:=true”. This will start the connection between the Kinect camera and ROS. The point cloud, depth image and RGB image of the Kinect camera will be available as ROS topics
  Point cloud - /camera/depth_registered/points
  Depth image - /camera/depth_registered/image_raw
  Color image - /camera/rgb/image_rect_color

## Slide 5: Procedure
Run “roslaunch rtabmap_ros rgbd_mapping.launch”. This will start RTAB-Map.
Move the Kinect camera slowly to map. The 3D map window changes colour based on how fast the camera is being moved:
  Black - The camera is being moved sufficiently slow
  Yellow - Warning. The camera is being moved fast. RTAB-Map might lose track of the camera’s location

## Slide 6: Procedure
    Red - RTAB-Map has lost track of the camera’s location. To start the mapping process again point the camera to a previously mapped location and click on the ‘Reset Odometry’ option in the Detection menu.
  Video link - https://youtu.be/eghTYsVoqck

## Slide 7: References
http://introlab.github.io/rtabmap/
https://en.wikipedia.org/wiki/Simultaneous_localization_and_mapping

## Slide 8
THANK YOU!